## Slide 1: Medical Imaging Formats
DICOM and NIfTI

## Slide 2: Installing New Libraries / Packages
If using anaconda / miniconda:
  conda install -c conda-forge pydicom nibabel
  Anaconda also has a GUI for managing libraries
If using python.org:
  pip install pydicom nibabel
  (pip also works in Anaconda, but it can lead to clashes)
If using uv:
  uv pip install pydicom nibabel
The “main” channel only has the most popular libraries
pydicom for DICOM files
nibabel for NIfTI (and others…)

## Slide 3: DICOM
The standard (imaging) format for medical imaging
  Stores image data and study metadata
  Mainly designed for compatibility and standardization
Very complex: has to be flexible enough to handle different vendors, modalities, metadata, etc.
Cannot handle raw data (e.g. CT sinogram, SPECT list mode, etc.) – those are usually proprietary formats
Most modalities output multiple DICOM files in 2D, even for n-D scans (e.g. for a 4D MRI volume+time)
  In practice: usually convert from DICOM to a more “convenient” format for further processing

## Slide 4
import pydicom
f = './data/xray-chest.dcm'
dcm = pydicom.dcmread(f)
print(dcm)
Location of the DICOM file
Print all the DICOM metadata
print(dcm['00081030'])
print(dcm['StudyDescription'])
print(dcm.StudyDescription)
print(dcm.get('StudyDescription'))
Different ways to access the metadata
val = dcm.XRayTubeCurrent * dcm.ExposureTime
print(f"{val / 1000} mAs")
Search the Internet for the DICOM tag definition

## Slide 5
import matplotlib.pyplot as plt
img = dcm.pixel_array
print(img.shape) # rows (height), columns (width)
plt.imshow(img)
Image matrix
≈7.5 megapixels!
samples = img.flat[::10]
_ = plt.hist(samples, 100)
Sample by getting every 10th value
_, (ax1, ax2) = plt.subplots(ncols=2)
ax1.imshow(img, vmin=700, vmax=2500, cmap='inferno')
ax2.imshow(img, vmin=2200, vmax=3600, cmap='inferno')
Colormap
Different window/levels

## Slide 6
from pathlib import Path
d_ct = Path("./data/ct-head")
f_lst = list(d_ct.glob("CT*"))
f_lst = sorted(f_lst)
print(f_lst)
Library for handling files and folders / directories / paths
Get all files named “CT*”
Sort in alphabetical order
import pydicom
dcm_lst = []
for f in f_lst:
dcm = pydicom.dcmread(f)
dcm_lst.append(dcm)
print(dcm_lst)
Load all the DICOM files into a list
What about loading 3D volumes (e.g. CT)?
How should we combine the 2D images → 3D volume?

## Slide 7
import numpy as np
print(dcm_lst[0].ImagePositionPatient)
pos_lst = []
for dcm in dcm_lst:
pos_lst.append(dcm.ImagePositionPatient)
pos_all = np.stack(pos_lst)
print(pos_all)
Image x,y,z position in the “patient coordinate system”
Stack up into a single 32x3 matrix
dist = pos_all[0] - pos_all
print(dist)
Get the x,y,z distance compared to the first position
dist = dist[:, 2]
print(dist)
In this specific case, it’s obvious the scans are captured along the z-axis

## Slide 8
idx = np.argsort(dist)
print(idx)
print(dist[idx])
Get the indexes in ascending order
img_lst = []
for n in idx:
img = dcm_lst[n].pixel_array
img_lst.append(img)
vol = np.stack(img_lst, axis=2)
print(vol.shape)
Get the 2D images in order …
… and stack them into a 3D volume
import matplotlib.pyplot as plt
samples = vol.flat[::10]
_ = plt.hist(samples, 100)
Sample every 10th value and get histogram
Air?
Soft tissue?
Bone?

## Slide 9
print(dcm.RescaleSlope)
print(dcm.RescaleIntercept)
vol = vol.astype(float)
vol = vol * dcm.RescaleSlope + dcm.RescaleIntercept
samples = vol.flat[::10]
_ = plt.hist(samples, 100)
Convert to floating point
Rescale to HU / CT numbers
_, ax_lst = plt.subplots(nrows=4, ncols=8, dpi=300)
n = 0
for n_row in range(4):
for n_col in range(8):
ax = ax_lst[n_row][n_col]
img = vol[:, :, n]
ax.set_axis_off()
ax.imshow(img, vmin=10, vmax=55, cmap='gray')
n += 1
Make figure higher res.
Window / level to ≈ brain tissue HU

## Slide 10
print(dcm.PixelSpacing)
print(dcm.SliceThickness)
print(dist[idx])
The resolution is not isotropic
_, ax_lst = plt.subplots(nrows=4, ncols=8, dpi=300)
n = 0
for n_row in range(4):
for n_col in range(8):
ax = ax_lst[n_row][n_col]
img = np.rot90(vol[:, n, :], k=3)
ax.set_axis_off()
ax.imshow(img, vmin=10, vmax=55, cmap='gray',
aspect=5/0.43)
n += 16
Multi-planar recontruction (sagittal view)
Slice at a different plane
Set aspect ratio to account for resolution difference
Rotate view
Only show every 16th slice

## Slide 11: NIfTI
Neuroimaging Informatics Technology Initiative
  Research format designed for 3D/4D medical imaging data
  Advantages: single file stores the entire volume
  Disadvantages: very limited metadata support (not even patient or study name!)
Use 3rd party software to convert DICOM to NIfTI
  E.g., dcm2nii, mriconvert, etc.
Python library nibabel supports NIfTI

## Slide 12
import nibabel as nib
nii = nib.load('./data/mri-heart.nii.gz')
print(nii)
NIfTI metadata is more limited
vol = nii.get_fdata()
print(vol.shape)
NIfTI can store 3D/4D volumes
print(nii.header['pixdim'])
In NIfTI, the x,y,z,t spacing / resolution info starts from index 1 (index 0 is for the qfac sign bit)

## Slide 13
_, ax_lst = plt.subplots(nrows=4, ncols=4, dpi=300)
n = 0
for n_row in range(4):
for n_col in range(4):
ax = ax_lst[n_row][n_col]
img = np.rot90(vol[:, :, n])
ax.set_axis_off()
ax.imshow(img, vmin=0, vmax=1500, cmap='gray')
n += 6
Only show every 6th slice
Rotate 90°
import numpy as np
import matplotlib.pyplot as plt
samples = vol.flat[::10]
_ = plt.hist(samples, 100)
plt.yscale("log")
Set histogram to log-scale

## Slide 14
We haven’t yet properly accounted for spatial resolution, relative positioning, orientation, or 4D (temporal) data, but this should be enough in many cases.